## Slide 1: BT201
20/10/2022
Biochemical Process Calculations
Energy Balance on closed and open system

## Slide 2
Energy balance for closed and open system
Based on Conservation of energy
  Energy can neither be created nor be destroyed
  Energy gained by a system must be exactly equal to the amount of energy lost by its surrounding
First law of thermodynamics
Only system that are homogeneous, not charged effects will be studied here

## Slide 3
Points to be remember
Heat:
  For adiabatic process (perfect insulation), Q=0
Work:
  Movement of system boundary against a resisting force
      Movement of piston, rotation of shaft
  If there is no moving part, then W=0
Kinetic energy
If system is not accelerating , then KE=0
Potential energy
If the system is not falling or rising, then PE=0 w.r.t reference
Internal energy
  Depends on the chemical composition, state of aggregation and temperature of the system
  Independent of pressure for ideal gases and nearly independent of pressure for solids and liquids
  If T and phase do not change, no reaction occurs and pressure change is less than a few atm, then ΔU=0

## Slide 4
Energy balance on closed system
  No mass flows in or out of the system
  Energy balance equation
Rate of Accumulation of energy =rate of input of energy – rate of output of energy
  Energy can transfer, so input and output terms exist
  Energy transferred in the form of heat (Q) and work (W)
  Accumulation : difference between the final and initial energies of the system
Q

## Slide 5
First law of thermodynamics for a closed system
Each term represents net cumulative amount over a specific time interval, not energy per time
  Convention use here:
  Q is positive when supply to the system
  W is positive when it is done by the system

## Slide 6
Example1

## Slide 7
An additional 100 J of heat is transferred to the gas as it expands and re-equilibrates at 100 C.

## Slide 8
Energy balance on open system at steady state
Mass crossing its boundaries as the process occurs.
Work must be done on such a system to push mass in, and work is done on the surroundings by mass that emerges.
  Mass entering: work done on the system
  Mass leaving: work done by the system
Both work terms must be included in the energy balance.

## Slide 9
Net work done

## Slide 10
Flow work

## Slide 11
The first law of thermodynamics for an open system at steady state has the form
Rate of Accumulation of energy =rate of input of energy – rate of output of energy
At steady state,
input = output
“Input” here signifies the total rate of transport of kinetic energy, potential energy, and internal energy by all process input streams plus the rate at which energy is transferred in as heat
“output” is the total rate of energy transport by the output streams plus the rate at which energy is transferred out as work
Cont.
Q
W

## Slide 12
Cont.
Q
W

## Slide 13
Cont.
Q
W

## Slide 14
Cont.
Q
W

## Slide 15
Cont.

## Slide 16
Cont.

## Slide 17
Cont.