## Slide 1: BT201
13/10/2022
Biochemical Process Calculations:
Multiphase system

## Slide 2
Multiphase in chemical/biochemical processes
Some process units in chemical/ biochemical industry accomplish physical separations, (do not involve reactions) in which components of mixture are separated into two or more fractions.
As a rule, separation/purification processes involve multiple phases are easy to perform. It is difficult to separate different components of a single phase.
Reactor/Bioreactor
(reaction)
multiphase: (Vapor-liquid)
Physical process
Top product
Bottom product
Involves: Liquid / gas / solid / immiscible / partially immiscible liquid

## Slide 3
Multiphase system example: distillation
Water + alcohol
Alcohol (99%)
+ water
Water + Alcohol (1%)
Distillation (vapor-liquid contact )
Separating high volatile component
--component from low volatile component
separation based on relative volatility
Example:
Product (ethanol, butanol) recovery from water (fermentation/distillery)
Refinery (get different fuels from crude petroleum)
Petrochemical (get ethylene oxide from ethylene oxide +water, get propylene from propylene +propane)

## Slide 4
MULTIPHASE SYSTEM EXAMPLE: ABSORPTION:
Absorption: mass transfer operation in which one or more species (solute) is removed from a gaseous stream by dissolution in a liquid
mass transfer: solute transfer from gas to liquid
Gas
(air + high CO2/SO2
Gas
(air + low CO2/SO2)
Liquid
(Water+ less or
no CO2/SO2)
+high solute
+high
solute
+low solute
+low solut
Liquid
(Water+ high CO2/SO2)

## Slide 5
Multiphase system example: Extraction
Liquid-Liquid extraction is a mass transfer operation in which a liquid solution (the feed) is contacted with an immiscible or nearly immiscible liquid (solvent) that exhibits preferential affinity or selectivity towards one or more of the components in the feed.
Example:
To separate closed-boiling point mixture that cannot withstand high temperature of distillation
Example:
Recovery of penicillin from fermentation broth; solvent: butyl acetate.
Perfumes, fragrances and essential oils
Recovery of acetic acid from dilute aqueous solutions; solvent: ethyl-acetate.

## Slide 6
Multiphase system example: Adsorption
Gas or liquid solutes selectively accumulates on the solid surface.
Solid surface
or liquid phase
Waste water treatment

## Slide 7
Multiphase
Absorption or scrubbing process: a separation process involving a gas in contact
with a liquid solution. For example, removal of sulfur dioxide from a gas stream.
Stripping process: a separation process involving a liquid in contact with a gas. (typically absorption and stripping columns run in parallel for regeneration of liquid solvent used in absorption process)
Adsorption: A separation process involving attraction of chemical species in gases or liquids to the surface of solids
Distillation: a separation process exploits the difference in vapor pressure by
partially vaporizing a liquid mixture, yielding a vapor relatively rich in some components and a residual liquid relatively rich in other components. For example, recovery of methanol from an aqueous solution.
Gasliquid
GasSolid Liquidsolid
Vaporliquid
liquidVapour
liquidgas

## Slide 8
Cont..
Liquid extraction: separation process exploits the difference in the miscibility of certain components in liquid among different liquid solvent. For example, separation of paraffinic and aromatic hydrocarbons.
Leaching: the operation of dissolving a component of a solid phase in a liquid solvent. For example, brewing a cup of coffee
Crystallization: a separation process exploits the difference in the freezing points of certain components. For example, separation of an isomeric mixture. Solute come out of from solution as solid crystal
Drying: mass is transferred as a vapor (from solid) into the surrounding gas
liquidliquid (immiscible/partially)
solidliquid
vapor (from solid) into the gas
solute (from
solution) as solid

## Slide 9
Phase equilibrium and phase diagram
Phase equilibrium: When species transfer from one phase to another, the transfer rate generally decreases with time until the second phase is saturated with the species, holding as much as it can hold at the prevailing process condition. When the concentration of all the species in each phase no longer changes with time, the phase are said to be in phase equilibrium.
A phase diagram of a pure substance is a plot of one system variable against another that shows the conditions at which the substance exists as a solid, a liquid, and a gas. The most common of these diagrams plots pressure on the vertical axis versus temperature on the horizontal axis. The boundaries between the single-phase regions represent the pressures and temperatures at which two phases may coexist.
phase 1I A, B…..
phase 1 A, B….

## Slide 10
Single component phase equilibrium
Pure water is placed in a leak proof cylinder fitted with movable piston
Pressure can be adjusted by varying force F
Heat can be added or withdrawn (for adjusting to any desired temperature)
The state of water follows the path A (V) B (V-L) C (L) D(L-V) E (V)
A phase diagram

## Slide 11
Several familiar terms may be defined with reference to the phase diagram.
If ( T, P) falls on the vapor–liquid equilibrium curve, P is the vapor pressure of the substance at temperature T, and T is the boiling point of the substance at pressure P .
-----If P=1 atm, T is called the normal boiling point of that substance.
If ( T, P) falls on the solid–liquid equilibrium curve, then T is the melting point or freezing point at pressure P.
If ( T, P ) falls on the solid–vapor equilibrium curve, then P is the vapor pressure of the solid at
temperature T, and T is the sublimation point at pressure P.
The point ( T, P) at which solid, liquid, and vapor phases can all coexist is called the triple point of the substance.
The vapor–liquid equilibrium curve terminates at the critical temperature and critical pressure and ( TC
and PC ). Above and to the right of the critical point, two separate phases never coexist.
Phase diagram……

## Slide 12
𝒑𝑨 = 𝒚𝑨 𝑷𝒕𝒐𝒕
𝑨
= 𝒙𝑨 𝒑∗ (𝑻 )
𝒑𝑨 = 𝒚𝑨 𝑷𝒕𝒐𝒕
= 𝒙𝑨 𝑯𝑨 (𝑻 )
𝑯𝑨 (𝑻 ): Henry’ Law constant for A in a specific solvent
Henry’s law is generally valid for solutions in which xA is close to 0 (dilute solutions of A ) provided that does not dissociate, ionize, or react in the liquid phase
Raoult’s law is an approximation that is generally valid when xA is close to 1 that is, when the liquid is almost pure A
Liquid
A+B+C
Vapour A +B+C
Raoult’s Law: Describe the vapour liquid equilibria of ideal solution
𝒚𝑨 : mole fraction of A in gas phase
𝒙𝑨 : mole fraction of A in liquid phase
𝑨
𝒑 : partial pressure of A in the gas phase
𝑨
𝒑∗ (𝑻 ): vapour pressure of A (depends on T)
Henry’ Law
Vapor-Liquid and gas liquid equilibrium calculation for ideal solution

## Slide 13
Important for liquid-vapor equilibrium
In distillation components are separated based on the relative volatility (top product: high volatility and bottom product: low volatility)
High vapour pressure high volatility
Low vapour pressure low volatility
Data: from table
For design need the Vapour pressure data at different temperature
vapour pressure of B
vapour pressure of A
Ptot
x
x
x x
yB
y
concentration ratio of A and Bin liquid phase
B
A
xA
B B
A A
Ptot
B B
xA
A
AB


  concentration ratio of A and B in vapour phase
p*
p*
p*
p*
  or 
Liquid A+B
mole fraction of A in liquid: xA or x
mole fraction of A in vapour: yA or y or y* at equilibrium
Vapour
A+B
T, Ptot
(α > 1 good separation)
FEED (A,B…)
Importance of vapor pressure (V-L equilibrium)



## Slide 14
=
𝑑𝑝∗ λ
𝑑𝑇 𝑇(𝑉𝑉 − 𝑉𝑙)
𝑉𝑉=molar volume (volume/mole) of vapor
𝑉𝑙=molar volume (volume/mole) of liquid
λ: latent heat of vaporization
𝑝∗: vapor pressure, T: temperature
Z: constant, different for
different substances
(Chemical potential are same in both
vapor and liquid phases)
VAPOR PRESSURE: CLAUSIUS-CLAPEYRON EQUATION

## Slide 15
Antoine Equation
𝐴, 𝐵 𝑎𝑛𝑑 𝐶: 𝑐𝑜𝑛𝑠𝑡𝑎𝑛𝑡
T: (°C),
𝒑∗: mmHg
VAPOR PRESSURE: Antoine Equation

## Slide 16
Degree of freedom: Gibbs phase rule
C=2 (for binary system, example ethanol (A) and water (B)) P=2 (the vapour and liquid phase)
F=2; So the system has two degree of freedom
mole fraction of A
A
in liquid: x or x
mole fraction of A in vapour: yA (y) or y*
Vapour A+B
T, P
t
Liquid A+B
Extensive variable: depends on the size of system
Example: mass, volume
Intensive variable: do not depends on the size
Example: temperature, pressure, density, specific volume, mass
and mole fraction of individual system components in each phase
Degree of freedom (DF) : number of intensive variables that must be specified for a system at equilibrium to calculate the remaining intensive variables
Gibb’s Phase rule: F=C-P+2,
F: Degree of freedom
C: number of component/chemical species P: the number of phases at equilibrium

## Slide 17
Pure liquid water:
P=1, C=1, F=1-1+2=2
Two intensive variables must be specified to fix the state of the system, for example, T and
P. Once these two variables have been specified, other intensive variables such as viscosity and density may be determined by nature
As F=2, two quantities need to be fixed to define the system in equilibrium.
if T and P are fixed , the liquid and vapour composition will be
t
automatically fixed if the system is in equilibrium.
If T and liquid composition are fixed ,the Pt and vapour composition
will be automatically fixed if the system is in equilibrium.
Liquid A+B
mole fraction of A in liquid: xA or x
mole fraction of A
in vapour: yA (y) or
y*
Vapour A+B T, Pt
The total number of parameters and variables: F=C-P+2 = 2-2+2 = 2
(Temperature (T), total Pressure(Pt), liquid composition and vapor composition)
Cont..

## Slide 18
A mixture of liquid, solid, and vapor water:
P=3, C=1, DF=2+1-3=0
No further information about the system is required, all intensive variables are fixed.
Three phases coexist at equilibrium at only one temperature and pressure
A vapor-liquid mixture of acetone and methyl ethyl ketone (MEK)
P=2, C=2, DF = 2 + 2 – 2 = 2
Two variables must be specified to fix the state of the system.
Setting T and P: can fixes the acetone and MEK mole fractions in both the vapor and liquid phases
Setting T and acetone mole fraction in vapor phase: P and acetone mole fraction in liquid are then
fixed
Cont..