## Slide 1: BT201
09/11/2022
Biochemical Process Calculations

## Slide 2
Changes in P at constant T and state of aggregation
Changes in T at constant P and state of aggregation
Phase changes at constant T and P-—melting, solidifying, vaporizing, condensing, sublimating
Mixing of two liquids or dissolving of a gas or a solid in a liquid at constant T and P
Pressure, T, composition, phase can be changed during process
Objective
Enthalpy and internal energy can be calculated for:
Introduction of non reactive process

## Slide 3
Calculating specific internal energy and specific enthalpy
Once we know how to calculate and for these four types of processes, we can calculate these quantities for process by taking advantage of the fact that and are state properties.
Procedure
  construct a hypothetical PROCESS PATH from the initial state to the final state.
  It could be consisting of a series of steps of the given FOUR types.
  we calculate and for each of the steps, and then add the and ’s for the steps to calculate and for the total process

## Slide 4
Suppose solid phenol at 25 °C and 1 atm is converted to phenol vapor at 300 ° C and 3 atm.
How to calculate and of the process?
If we had a table of enthalpies for phenol, we could simply subtract at the initial state from at the final state
If not available?
How to solve

## Slide 5
Do not have such a table.
Our task is then to construct a hypothetical process path from the solid at 25 °C and 1 atm to the vapor at 300 °C and 3 atm.
  How to construct hypothetical path
  What are the constrained to be followed?
    In the process, T, P, phase are changing
    Each step in the hypothetical path should have only one of these three factor changing
    Phase change should happen at temperature where enthalpy associated with phase change available in handbook

## Slide 6
Procedure:
What are the melting and boiling point of the compound?
Note that enthalpy changes for the melting of phenol at 1 atm and 42.5 °C (the normal melting point of phenol) available
For the vaporization of phenol at 1 atm and 181.4 ° C (the normal boiling point of phenol) available.
We therefore choose this hypothetical process path

## Slide 7
Notice that in this path, the first, third, and fifth steps are Type 2 (change in T at constant P ),
the second and fourth steps are Type 3 (change in phase at constant T and P ),
sixth step is Type 1 (change in P at constant T )
Also notice that the phase changes were made to occur at the conditions for which tabulated enthalpy changes are available.

## Slide 8
Energy balance procedure
Perform all required material balance calculations
Write the appropriate form of the energy balance (closed or open system) and delete any of the terms that are either zero or negligible for the given process system.
Choose a reference state—phase, temperature, and pressure—for each species involved in the process.
For a closed constant- volume system, construct a table with columns for initial and final amounts of each species and specific internal energies relative to the chosen reference states. For an open system, construct a table with columns for inlet and outlet stream component flow rates and specific enthalpies relative to the chosen reference states.

## Slide 9
5. Calculate all required values of and insert the values in the appropriate
places in the table.
6.
7. Calculate any work, kinetic energy, or potential energy terms that you have not dropped
from the energy balance.

## Slide 10
Energy Balance on a Condenser

## Slide 14
At constant T,
Later, we will learn

## Slide 18
process