## Slide 1: BT201
03/08/2022
Biochemical Process Calculations

## Slide 2
In the process industries, process streams are normally delivered to or removed from a process in pipes. The flow rate of a process stream is the rate at which material is transported through a carrying pipe/ process line/stream.
The flow rate of a process stream may be expressed as a (mass/time) or as a (volume/time). Suppose a fluid (gas or liquid) flows in the cylindrical pipe, where the shaded area represents a section perpendicular to the direction
The mass flow rate () of a process stream is the mass (m) transported through a pipe per unit time (t):
The molar flow rate () of a process stream is the moles (n) of a substance transported through a pipe per unit time:
The volumetric flow rate () of a process stream is the volume (V) transported through a line per unit time:
Process stream flowrate
F (moles fluid /s)
)

## Slide 3
Suppose a gas is flowing through a cone-shaped pipe.
  How do the mass flow rates of the gas at the inlet and outlet compare? (Remember the law of conservation of mass.)
  If the density of the gas is constant, how do the volumetric flow rates at these two points compare?
  What if the density decreases from inlet to outlet?
Cont..
F (moles fluid /s)
)
However, the mass and the volume of a fluid—in this case, the fluid that passes through the cross section each second—are not independent quantities but are related through the fluid
Density (), :

## Slide 4
Orifice meter: The orifice meter is an obstruction in the flow channel with a narrow opening through which the fluid passes. The fluid pressure drops (decreases) from the upstream side of the orifice to the downstream side; the pressure drop (which may be measured with a number of devices, including a differential manometer) varies with the flow rate—the greater the flow rate, the larger the pressure drop.
A flowmeter is a device mounted in a process line that provides a continuous reading of the
flow rate in the line. Two commonly used flowmeters:
Rotameter : The rotameter is a tapered vertical tube containing a float; the larger the flow rate, the higher the float rises in the tube.
Rotameter
Orifice meter
Cont..

## Slide 5
Fundamental of material balances
System and surrounding
System is any arbitrary portion of or a whole process you want to consider for analysis.
You can define a system such as a reactor, a section of a pipe, or an entire refinery by stating in words what the system is.
Or you can define the limits of the system by drawing the system boundary, which is a line that encloses the portion of the process that you want to analyze.
The boundary could coincide with the outside of a piece of equipment or some section inside the equipment.
Surrounding: Anything outside the system boundary

## Slide 6
Type of system
Closed system: No mass exchange with surrounding
Open system: material crosses system boundary

## Slide 7
Process classification
Based on how material crosses system boundary
Batch: The feed is charged (fed) into a vessel at the beginning of the process and the vessel contents are removed at the end of process. No mass crosses the system boundaries between the time the feed is charged and the time the product is removed. Rapidly add reactants to a tank and remove the products and unconsumed reactants at the end
Continuous: The inputs and outputs flow continuously throughout the duration of the process. Pump a mixture of liquids into a distillation column at a constant rate and steadily withdraw product streams from the top and bottom of the column. Continuous stirred tank reactor
Semi-continuous: Any process that is neither batch nor continuous. Allow the contents of a pressurized gas container to escape to the atmosphere; slowly blend several liquids in a tank from which nothing is being withdrawn.
Fed batch: . Special case of semi continuous, only in (intermediate feeding, may be discrete way or continuous), fed batch reactor use in antibiotic production

## Slide 8
Cont.
Based on changes to process variables
Steady state process:
If the values of all the variables in a process (i.e., all temperatures, pressures, volumes, flow
rates) do not change with time, except possibly for minor fluctuations about constant mean
values, the process is said to be operating at steady state
Unsteady state or transient process: If any of the process variables change with time, transient or unsteady-state operation is said to exist.
By their nature, batch and semi batch processes are unsteady-state operations, whereas continuous processes may be either steady-state or transient for short duration.
Batch processing is commonly used when relatively small quantities of a product are to be produced on any single occasion, while continuous processing is better suited to large production rates.
Continuous processes are usually run as close to steady state as possible; unsteady-state (transient) conditions exist during the start-up of a process

## Slide 9
A car tire is filled with air at a steady rate of 10 g/min.
  Material crosses the boundary  open system
  Only input and no output semi batch (fed batch)
  Process variable such as pressure and volume changes with time unsteady state process
A bottle of milk is taken from the refrigerator and left on the kitchen table.
  Material does not crosses the boundary  closed system
  no input and no output batch
  Process variable such as temperature is changes with time unsteady state process
Water flowing through a pipe with fixed diameter
  Material crosses the boundary  open system
  Both input and output continuous
  No changes of process variables value steady state
Cont.

## Slide 10
Material balances: law of conservation of mass
Total mass of a closed system is constant
Mass can not be created or destroyed
For a chemical reaction
    Mass of reactant =mass of product
Fundamental basis of material balance

## Slide 11
What can happen to a materials entering the system?
Leaves the system
Stays in the system
Converted to another form by reaction
    get consumed and new materials are formed
Cont.

## Slide 12
Terms
Input: material entering the system
Output: material leaving the system
Accumulation: material staying in the system
Consumption: due to reaction
Formation/generation: raw material formed in the system due to other reaction
Equation
Rate of accumulation ═ Rate of in — Rate of out + Rate of generation — Rate of consumption
Accumulation
Generation
Consumption
Input:
Output:
Cont.

## Slide 13
Types of material balances
Total material balance
  Combination of all the component balance
    Total mass does not change, in-out=accumulation
Component balance
  Each component balance
  Non reactive/inert component, consumption=0, generation=0
At steady state
  accumulation=0
Accumulation
Generation
Consumption
Input:
Output:

## Slide 14
Degree of freedom (dof) analysis
To check the solvable or not
After calculation you may find out that there is not enough information
To avoid it do degree of freedom analysis
Method
    Draw flowchart and label it
    All the information associated with problem incorporate in the flowchart
    Mention/entered all the relationship
  How many unknown variables on the flow chart
  Count number of independent equation related with these unknown variables

## Slide 15
DOF ═ number of unknown — number of independent equation
If DOF ═ 0,
  Problem can be solved
If DOF > 0
  More unknown than independent equation
  At least DOF number of variables need to be fixed to solve the problem
If DOF < 0
  More independent equation than unknown
  Over specified with redundant equations
Cont.

## Slide 16
Solving a material balance problem
Choose a basis for calculation
  Appropriate basis = Easy calculation
How to choose
    What information are given
    What do I need to find?
  If flow rate or mass is given use it as basis
  If not specified assume a convenient amount or flow rate
  Try to use mass flow rate instead of volumetric flow rate as basis
Mention the basis in flowchart
Write down all the independent equations with
Do DOF analysis and solve the equations